Preventative Maintenance Job Description:

Kitchen Equipment (yearly)

Clean Coils		Lube motors				Check belts adjust and replace

Check for leaks 	Change filters on water filters	 	Replace elements when needed

Walk-in Coolers (yearly)

Clean coils

Lube motors

Check for leaks

Booster Heaters  (yearly)

Clean with delime and descale cleaner

Steamers  (yearly with State Boiler Inspector)

Delime and descale

Replace anodes

Replace seals

Check for leaks

Cooling Towers at the following locations:

Lakewood Elementary School

James T. Alton Middle School

Meadowview Elementary School

North Hardin High School (3)

Parkway Elementary School

New Highland Elementary School

Bluegrass Middle School

Lincoln Trail Elementary School

Central Hardin High School (2)

Preventative Maintenance required for the above cooling towers:

Delime and remove scale

Lubed pumps and shafts

Check, adjust and replace belts

Lube, adjust, and repair louvers

Pipe and maintain chemical feeders

Weekly monitoring of chemicals

Check for leaks with the water system (float valves)

Heat Pumps

Clean coils		Lube motors and shafts	Check, adjust and replace belts

Clean strainers		Check for leaks

HVAC

Replace and clean window air conditioners

Assist when work overflow for HVAC positions in Maintenance