Tuesday, April 14, 2015

Hardin County Board of Education

Attn:  Gary Milby

65 W.A. Jenkins Road

Elizabethtown, KY. 42701

RE:  2015 Asphalt Resurfacing (Multiple Locations)

Hardin County Board of Education

KDE BG# 13-019

Mr. Milby:

Bids on the above referenced project have been reviewed.  Bid Tabulation is as follows on the enclosed spreadsheet.

Bus Garage Compound

Apparent Low Bidder – Scotty’s Contracting & Stone LLC.

Apparent Low Base Bid - $199,288.00

Alternate #2 Bid - $20,057.00

Alternate #3 Bid - $94,404.00

Must select either Alternate #2 or Alternate #3 bid and add to base bid.

Alternate #2:  Mill approx. 29,000 SF. area and install 1 ½” asphalt surface overlay at Bus Garage Compound

Construction required as a portion of Alternate #2 shall include and be limited to the milling 1 ½” of existing asphalt from the approx. 29,000 sf. area and installation of the 1 ½” asphalt surface overlay over the approx. 29,000 sf. area.  The existing finished grades and existing pavement thickness will remain the same as the existing conditions.

Alternate #2 essentially is an overlay of the existing asphalt pavement and does not provide any additional pavement thickness, strength, or longevity.  Eventually this area will need to be excavated to original grade and will require full depth stone and asphalt pavement.

Alternate #3:  Full depth pavement installation of approx. 29,000 SF. area at Bus Garage Compound

Construction required as a portion of Alternate #3 shall be as follows:

Saw cut existing asphalt pavement along “mill line” and adjacent areas as required.  Remove and dispose of existing asphalt pavement and stone base within this area, (approx. 29,000 sf.).  Grade area as required for full depth pavement section, (see general note 5), and to match proposed spot elevations as shown.  Install full depth stone and asphalt pavement section to match proposed spot elevations.

Alternate #3 provides for a new full depth stone and asphalt pavement section.  Due to the amount of and type of traffic at this site the entire parking area will eventually need to be re-constructed in this manner.

Central Office

Apparent Low Bidder – Hall Contracting of Kentucky, Inc.

Apparent Low Base Bid - $71,094.65

Central Hardin High School

Apparent Low Bidder – Scotty’s Contracting & Stone LLC.

Apparent Low Base Bid - $379,199.00

North Park Elementary School

Apparent Low Bidder – Hall Contracting of Kentucky, Inc.

Apparent Low Base Bid - $180,542.21

West Hardin Middle School

Apparent Low Bidder – Hall Contracting of Kentucky, Inc.

Apparent Low Base Bid - $43,640.10

Alternate #1 Bid - $40,305.25

If choose to accept Alternate #1, add to Base Bid.

Alternate #1:  Construct additional parking area. (20 additional parking spaces)

Based upon the Engineer’s Estimates, and the other bids received, the low bids appear to be fair and reasonable.  Upon review of the contractor’s previous performance, references, warranties, and list of sub-contractors in the Form of Proposal, both Hall Contracting of Kentucky, Inc. and Scotty’s Contracting & Stone LLC. appear to be qualified for the projects.  Upon discussions with both contractors, they are satisfied with their bids and the timing of the projects.

The BG-1 Form for the project, including construction contingences, illustrates the probable construction costs of $1,696,800.00.

If you have any questions, please feel free to contact me.

Respectfully Submitted,

Engineering Design Group, Inc.

Michael P. Billings PE, PLS