Nelson Co. Board of Education Energy Conservation Program

Guidelines

The primary goal of our energy management program is to provide a “comfortable learning environment” for the students of the Nelson County School system.  We must understand that this concern will be concentrated during the times that our buildings are occupied by our students and staff, while looking to unoccupied times in order to initiate savings in terms of energy consumption.  It makes no sense to heat or cool our buildings around the clock.  Our resources are not unlimited, so we need to make a conscious effort to save energy dollars whenever we have a chance as long as we do not sacrifice the learning environment.  Basically it boils down to the fact that we can use our resources (money) to heat and cool our buildings or we can use our resources to educate the children of our district.  Becoming an “energy saver” is good for the environment as well; there simply is not an inexhaustible supply of energy in our world.  In addition energy costs are on the rise, so unless we look for ways to conserve on energy costs they will continue to rise and our budgets will be under greater pressure

These guidelines are a recommendation for District Energy Conservation Standards, and designate responsibilities for the implementation of District Energy Guidelines.  Classrooms, offices, libraries, music rooms, and auditoriums will be controlled to maintain 70°F in the winter, and 74°F in the summer.  Summer and winter set points will be determined by energy management and maintenance based on actual temperatures and forecasts.  Each school will be individually set based on the heating and cooling system in the buildings.  Night setback and setup temperatures will be determined by energy management and maintenance in order to maintain a comfortable learning environment and maximize the use of the districts’ energy dollars.  Gyms and athletic facilities will have different set points based on usage.  Occupancy times for the District will be from 7:00am till one-half hour after the buses run, Monday through Friday.  Some changes to this schedule will be made for specific areas such as offices, daycares, and scheduled after school activities.

All spaces will be considered unoccupied during holidays, scheduled school breaks, conferences etc. unless energy management or maintenance is notified ahead of time.  Energy management and maintenance will utilize the occupied/unoccupied program and/or the optimal start program to assure that employees adhere to the following guidelines.

I appreciate the opportunity that the Nelson Co. Board of Education has provided for me as Energy Manager for the District.  I am looking forward to helping the District to maximize the use of their energy dollars, while maintaining a proper learning environment for our students.

Sincerely,

John Peterson, Energy Manager

Guidelines

(Energy Conservation and Building Management)

Responsibilities:

- Every person is expected to be an "energy saver" as well as an "energy consumer. "

- The Teacher is responsible for implementing the guidelines during the time that he/she is present in the classroom.

- The Custodian is responsible for control of common areas, i. e. halls, cafeteria, etc.

- Since the custodian is typically the last person to leave a building in the evening, he/she is responsible for verification of the nighttime shutdown.

- The Principal is responsible for the total energy usage of his/her building.

- The Energy Manager performs routine audits of all facilities and communicates the audit results to the appropriate personnel

- The Energy Manager is responsible for either directly or indirectly making adjustments to the District's EMS, including temperature settings and run times for HVAC and other controlled equipment.

- The Energy Manager provides regular reports to Principals and the Superintendent indicating performance with regards to energy savings.

•   The District is committed to and responsible for maintenance of the learning

environment.

•   The District shall develop and implement a preventive maintenance and monitoring plan for its facilities and systems, including HVAC, building envelope, and moisture management.

______________________________________________________________________

GENERAL GUIDELINES

- Classroom doors should remain closed when HVAC is operating. The doors between conditioned space and non-conditioned space should remain closed at all times (i.e. between hallways and gym area).

- Proper and thorough utilization of data loggers should be initiated and maintained to monitor relative humidity, temperature, and light levels throughout the district's buildings to ensure compliance with district guidelines.

- All exhaust fans should be turned off every day and during unoccupied hours.

- All office machines (copy machines, laminating equipment, etc.) should be switched off each night and during unoccupied times. Fax machines should remain on.

- All computers should be turned off each night. This includes the monitor, local printer, and speakers. Network equipment is excluded.

- All capable PC's should be programmed for the "energy saver" mode using the power management feature. If network constraints restrict this for the PC, the monitor should go into the "sleep mode" after 10-minutes of inactivity.

- Only the Superintendent/designee may make exceptions to these general guidelines.

Page 1 of 4

Guidelines

(Energy Conservation and Building Management)

Cooling Season Occupied Set Points 1:

Unoccupied Set Point:

Unoccupied Set Point for Geo-Thermal Systems:

Preferred Cooling Season Set Point:

Heating Season Occupied Set Points 1:

Unoccupied Set Point:

Unoccupied Set Point for Geo-Thermal System:

Preferred Heating Season Set Point:

74°F -78°F 80°F

80°F

74°F

68°F -72°F 60°F

60°F

70°F

1 - Set points are in accordance with ASHRAf 55 "Thermal Conditions for Human Occupancy"

AIR CONDITIONING EQUIPMENT

- Occupied temperature settings should NOT be set below 74°F.

- During unoccupied times, the air conditioning equipment should be off. The unoccupied period begins within one-half hour after the students leave the area at the end of the school day. It is anticipated that the temperature of the classroom will be maintained long enough to afford comfort for the period the teacher remains in the classroom after the students have left.

- Air conditioning start times may be adjusted (depending on weather) to ensure classroom

comfort when school begins.

- Outside air dampers should be closed during unoccupied times.

- Blinds should be closed at the end of each school day.

- Ceiling fans should be operated in all areas that have them.

- Relative humidity levels should not exceed 60% for any 24-hour period.

- Air conditioning should not be utilized in classrooms during the summer months unless the classrooms are being used for summer school or year-round school. Air conditioning may be used by exception only or in those schools that are involved in team-cleaning.

- In all areas which have evaporative coolers such as shops, kitchens and gymnasiums, the doors leading to halls which have air conditioned classrooms or dining areas should be kept closed as much as possible.

- Where cross-ventilation is available, during periods of mild weather, personnel should shut down HVAC equipment and adjust the temperature with the windows and doors. Cross-ventilation is defined as having windows and/or doors to the outside on each side of a room.

- Dry food storage areas should be maintained within code requirements. Typically, this is 55°F -75°F temperature with 35%-60% Relative Humidity.  Data loggers will be used to verify compliance.

Page 2 of 4

Guidelines

(Energy Conservation and Building Management)

Heating Equipment

- Occupied temperature settings should NOT be above 72°F.

- The unoccupied temperature setting shall be 60°F (i.e. setback).

- The unoccupied time shall begin within one-half hour after the students leave an area.

- During the spring and fall when there is no threat of freezing, all steam and forced air heating systems should be switched off during unoccupied times.  Hot water heating systems should be switched off using the appropriate loop pumps.

- All domestic hot water systems should be set no higher than 120°F to 140°F for cafeteria service (with a dishwasher booster).

- All domestic hot water re-circulating pumps should be switched off during unoccupied times.

- For heat pumps, a 6°F dead-band between heating and cooling modes should be used.

- Heating oil and propane (if applicable) levels should be physically measured and recorded by “sticking the tanks” at least on the following intervals: 1) recurring scheduled monthly date, 2) immediately before delivery, 3) immediately after delivery.

Lighting

- All unnecessary lighting in unoccupied areas should be turned off.  Teachers should make certain that lights are turned off when leaving the classroom empty.  Lights should be turned off when leaving the room empty for more than a couple of minutes.  Utilize natural lighting when appropriate (open the blinds).

- All outside lighting should be off during daylight hours.

- Gym lights should not be left on unless the gym is being utilized.

- All lights should be turned off when students and teachers leave school.  Teachers should turn off the lights in their classroom when they leave each day.

- Custodians should utilize a half-light program in their schools each day at approximately 4:00 pm.  In addition custodians should turn on lights only in the areas in which they are working.

- Lights should be turned on only when they are definitely needed.  Remember that lights consume electricity, but also give off heat that places an additional load on the air conditioning equipment that again increases the use of electricity needed to cool the room.

Page 3 of 4

Guidelines

(Energy Conservation and Building Management)

Water

- All plumbing and/or roof leaks should be reported and repaired immediately.

- Grounds watering (irrigation) should only be done between 4am-10am.  Watering should not occur during the heat of the day (typically between 10am-8pm).

- When spray irrigating, the water should not directly hit the building.

- Ensure water sub-meters are installed on irrigation and cooling tower supply lines to eliminate sewer charges.

Disclaimer: The district shall adopt, observe and implement these guidelines as provided. However, these guidelines are not intended to be all-inclusive, and they may be modified for local conditions. These guidelines supersede all previous instructions related to energy conservation or building management.

Conservation Guidelines 9.15.06                                                                                                  Page 4 of 4